## Slide 1: 8085 Architecture & Its Assembly language programming
Dr A Sahu
Dept of Computer Science & Engineering
IIT Guwahati

## Slide 2: Outline
8085 Era and Features
8085
  Block diagram (Data Path)
  Bus Structure
  Register Structure
Instruction Set of 8085
Sample program of 8085
Simulator & Kit for 8085

## Slide 3: 8085 Microprocessor
8 Bit CPU
3-6Mhz
Simpler design: Single Cycle CPU
ISA = Pre x86 design (Semi CISC)
40 Pin Dual line Package
16 bit address
6 registers: B, C, D, E, H,L
Accumulator 8 bit

## Slide 4
W
Z
B
C
D
E
H
L
SP
PC
Inc/Dec. ter
Add latch
MUX
Bus 8 Bit
Interrupt Control
Serial I/O Control
IR
I Decode
&
M/C
Encoding
tmp R
ACC
Timing and Control
ALU
Add Buff
Data/Add Buff
Flag
INTR
INTA
RST5.5
ReSeT6.5
RST7.5
TRAP
SID
SOD
8085 Microprocessor Architecture

## Slide 5
The 8085 Bus Structure
8085
MPU
A15
A0
D0
D7
Address Bus (16bit)
Memory
I/P
Data Bus (8bit)
O/P
Control Bus (8bit)

## Slide 6: 8085 Bus Structure
Address Bus : Consists of 16 address lines: A0 – A15
  Address locations: 0000 (hex) – FFFF (hex)
  Can access 64K ( = 216 ) bytes of memory, each byte has 8 bits
  Can access 64K  8 bits of memory
  Use memory to map I/O, Same instructions to use for accessing I/O devices and memory
Data Bus : Consists of 8 data lines: D0 – D7
  Operates in bidirectional mode
  The data bits are sent from the MPU to I/O & vice versa
  Data range: 00 (hex) – FF (hex)
Control Bus:
  Consists of various lines carrying the control signals such as read / write enable, flag bits

## Slide 7: 8085 Registers
Registers:
  Six general purpose 8-bit registers: B, C, D, E, H,L
  Combined as register pairs to perform 16-bit operations: BC, DE, HL
  Registers are programmable (load, move, etc.)
Stack Pointer (SP)
Accumulator & Flag Register
  (Zero, Sign, Carry, Parity, AuxCarry)
Program Counter (PC)
  Contains the memory address (16 bits) of the instruction that will be executed in the next step.
B
C
D
E
H
L
SP
PC

## Slide 8: How instruction executed
All instructions (of a program) are stored in memory.
To run a program, the individual instructions must be read from the memory in sequence, and executed.
  Program counter puts the 16-bit memory address of the instruction on the address bus
  Control unit sends the Memory Read Enable signal to access the memory
  The 8-bit instruction stored in memory is placed on the data bus and transferred to the instruction decoder
  Instruction is decoded and executed

## Slide 9: Instruction Set of 8085
Arithmetic Operations
  add, sub, inr/dcr
Logical operation
  and, or, xor, rotate, compare, complement
Branch operation
  Jump, call, return
Data transfer/Copy/Memory operation/IO
  MOV, MVI, LD, ST, OUT

## Slide 10: Copy/Mem/IO operation
MVI R, 8 bit // load immediate data
MOV R1, R2 // Example MOV B, A
MOV R M // Copy to R from 0(HL Reg) Mem
MOV M R // Copy from R to 0(HL Reg) Mem
LDA 16 bit // load A from 0(16bit)
STA 16 bit // Store A to 0(16bit)
LDAX Rp // load A from 0(Rp), Rp=RegPair
STAX Rp // Store A to 0(Rp)
LXI Rp 16bit // load immediate to Rp
IN 8bit // Accept data to A from port 0(8bit)
OUT 8 bit // Send data of A to port 0(8bit)

## Slide 11: Arithmetic Operation
ADD R // Add A = A + B.reg
ADI 8bit // Add A= A + 8bit
ADD M // Add A=A + 0(HL)
SUB R // Sub A = A -B.reg
SUI 8bit // Sub A= A - 8bit
SUB M // Sub A=A - 0(HL)
INR R // R = R+1
INR M // 0(HL)=0(HL)+1
DCR R // R = R-1
DCR M // 0(HL)=0(HL)-1
INX Rp // Rp=Rp+1
DCX Rp // Rp=Rp-1

## Slide 12: Other Operations
Logic operations
  ANA R ANI 8bit ANA M
  ORA, ORI, XRA, XRI
  CMP R // compare with R with ACC
  CPI 8bit // compare 8 bit with ACC
Branch operations
  JMP 16bit, CALL 16 bit
  JZ 16bit, JNZ 16bit, JC 16bit, JNC 16 bit
  RET
Machine Control operations
  HLT, NOP, POP, PUSH

## Slide 13: Assumption
RAM Memory is interfaced
Instructions are stored in memory
One I/O display port is interfaced to display data of ACC

## Slide 14: Simple Assembly Program
MVI A, 24H // load Reg ACC with 24H
MVI B , 56H // load Reg B with 56H
ADD B // ACC= ACC+B
OUT 01H // Display ACC contents on port 01H
HALT // End the program
Result: 7A (All are in Hex)
DAA operation for Decimal Adjust A+6=10H

## Slide 15: Flowchart to multiply two number
Start
LDA 2000 // Load multiplicant to accumulator
MOV B,A // Move multiplicant from A(acc) to B register
LDA 2001 // Load multiplier to accumulator
MOV C,A // Move multiplier from A to C
MOV C,A // Move multiplier from A to C
MVI A,00 // Load immediate value 00 to ACC
ADD B // Add B(multiplier) with A
DCR C // Decrement C, it act as a counter
JNZ L // Jump to L if C!=0
STA 2010 // Store result in to memory
HLT // End

## Slide 16: Code to multiply two number
LDA 2000 // Load multiplicant to accumulator
MOV B,A // Move multiplicant from A(acc) to B register
LDA 2001 // Load multiplier to accumulator
MOV C,A // Move multiplier from A to C
MVI A,00 // Load immediate value 00 to a
L: ADD B // Add B(multiplier) with A
DCR C // Decrement C, it act as a counter
JNZ L // Jump to L if C reaches 0
STA 2010 // Store result in to memory
HLT // End

## Slide 17: Factorial of a Program
LXI SP, 27FFH ; Initialize stack pointer
LDA 2200H ; Get the number
CPI 02H ; Check if number is greater than 1
JC LAST
MVI D, 00H ; Load number as a result
MOV E, A
DCR A
MOV C,A ; Load counter one less than number
CALL FACTO ; Call subroutine FACTO
XCHG ; Get the result in HL // HL with DE
SHLD 2201H ; Store result in the memory // store HL at 0(16bit)
JMP END
LAST: LXI H, 000lH ; Store result = 01
END: SHLD 2201H
HLT

## Slide 18: Sub Routine for FACTORIAL
FACTO: LXI H, 0000H
MOV B, C ; Load counter
BACK: DAD D // double add ; HL=HL+DE
DCR B
JNZ BACK ; Multiply by successive addition
XCHG ; Store result in DE // HL with DE
DCR C ; Decrement counter
CNZ FACTO ; Call subroutine FACTO
RET ; Return to main program

## Slide 19: 8085 Simulator & Kit
8085 Simulator is available
  Course website
8085 Kit is available in HW Lab (CS422)
  First test the program on Simulator and then go for the HW
  Sometime Kit have Driver, IDE and Assembler