## Slide 1: Robot Architectures
Presented By
Deepanwita Roy(20CSE024)

## Slide 2: Robot Architecture is the combination and disposition of the different kind of joints
that configure the robot kinematical chain.
Five common body-and-arm configurations:
Polar coordinate body-and-arm assembly.
Cylindrical body-and-arm assembly.
Cartesian
3. coordinate body-and-arm assembly.
Joined-arm
4. body-and-arm assembly.
5. Selective Compliance Assembly Robot Arm (SCARA).

## Slide 3: Polar coordinate body-and-arm assembly
Notation RRP
Consist of sliding arm (P joint) actuated related
rotate
to the body, which can about
both
vertical axis (R joint) and
a
(R
horizontal axis
joint)

## Slide 4: Work Envelope
The gross work envelope of a robot is defined as the locus of points in three
dimensional space that can be reached by the wrist.
Positioning axes (Major axes)
N. B. Work space is basically subset of work envelope.

## Slide 5: Polar Work Space

## Slide 6: Polar robot characteristics
Joints:
Rotation θ
Rotation φ
Linear ρ
Advantages:
Large reach
from a central support
●
It can bend to reach objects on the floor
Motor 1 and 2 close to the base
Drawbacks:
Complex kinematics model
Difficult to visualize

## Slide 7: Cylindrical body-and-arm assembly
Notation RPP
Consists of a vertical column, relative to
arm
which an assembly is
moved up or
down.
The arm can be moved in or out relative to
the column.

## Slide 8: Cylindrical Work Space

## Slide 9: Cylindrical Robot Characteristics
Advantages:
●
●
●
Simple kinematical model
Easy to display
Good accessibility to
cavities an d open
machines
Large forces when using hydraulic actuators
Drawbacks:
Restricted working volume
Requires guides protection (linear)
Joints:
Rotation θ
Linear Z
Linear ρ

## Slide 10: Cartesian coordinate body-and-arm assembly
PPP
Notation
Consists of three sliding joints
Other names include rectilinear robot and
X-Y-Z
robot

## Slide 11: Cartesian Work Space

## Slide 12: Cartesian Robot Characteristics
Linear movement in three dimensions |  |  | 
Si | mple kinemati |  | cal model
Rigid structure |  |  | 
Easy to display |  |  | 
Advantages:
●
●
●
●
Possibility of using cheap pneumatic actuators in pick and place operations
Drawbacks:
Requires a large robot volume which is greater than working
volume
Guides protection
Joints:
Linear X
Linear Y
Linear Z

## Slide 13: Joint-Arm body-and-arm assembly
Notation is RRR
3D rotation
General configuration of human arm
Basic angular work space

## Slide 14: Observation
First rotation θ1
Second rotation θ2
Third rotation θ3
Advantages:
maximum flexibility |  | 
large working volume |  | with respect to the robot s (angular)
joints easy to protect |  | 
can reach the upper and lower side of an object |  | 
complex kinematical model
linear movements are difficult
no rigid structure when stretched
Drawbacks
Joint Angles

## Slide 15: SCARA Robot
Notation RRP
SCARA stands for Selective Compliance Assembly Robot Arm
Similar to jointed-arm robot except that vertical axes are used
for shoulder and elbow joints to be compliant in horizontal
direction for vertical insertion tasks

## Slide 16: SCARA Robot
.

## Slide 17: SCARA Robot Characteristics
.
Robot | Joints | Observations
SCARA | rotation θ1 rotation θ2 rotation θ3 | Advantages: -high speed and precision Drawbacks: -only vertical axes

## Slide 18
.
Thanks